## Slide 1: Smart lightning system using CAN protocol
E1-DESD

## Slide 2: INTRODUCTION
The Smart Lighting System using CAN protocol is an embedded system designed to provide intelligent and efficient lighting control.
It uses the CAN (Controller Area Network) protocol for fast, reliable, and noise-immune communication between different lighting nodes.
The system can automatically control lights based on sensor inputs such as LDR, PIR, or ultrasonic sensors.
ESP32 is used as the main controller to process sensor data and manage communication. CAN ensures real-time data transfer even in harsh electrical environments. The system helps in reducing power consumption by switching lights only when required. It supports centralized monitoring and control of multiple lighting units. The project is suitable for applications like smart buildings and street lighting.

## Slide 3: CAN Architecture in Smart lighting system

## Slide 4: Information about the Sensors that used:-
IR (Infrared) Sensor
Working range: ~2 cm to 30 cm (depends on module and surface).
Operating voltage: 3.3 V – 5 V.
Input pin (to MCU): GPIO input pin (e.g. PB0)
Output from sensor: Digital (HIGH / LOW)
Data type sent on CAN: Object detected / not detected (1 or 0)
Use in this project: Detects presence/motion near the light to turn it ON/OFF.
Other applications: Obstacle detection, line follower robots, object counters.

## Slide 5
Ultrasonic Sensor (HC-SR04 type)
Trigger pin (output from MCU): GPIO output (e.g. PB1)
Echo pin (input to MCU): GPIO input / Timer input capture (e.g. PB2)
Output from sensor: Pulse width proportional to distance
Data type sent on CAN: Distance value (in cm)

## Slide 6
LDR (Light Dependent Resistor)
Working range: Depends on light intensity (lux-based).
Operating voltage: Used with 3.3 V or 5 V via voltage divider.
Current consumption: Very low (microamp range).
Output: Analog (resistance varies with light).
Other parameters: Resistance decreases as light increases.
Use in this project: Detects day/night condition for automatic light control.
Other applications: Automatic street lights, brightness control, solar systems

## Slide 7
Servo Motor
Working range: 0° to 180° (standard servo).
Operating voltage: 4.8 V – 6 V.
Control pin (output from MCU): PWM pin (e.g. PA8 / TIM1_CH1)
Input to servo: PWM signal (50 Hz)
Data source: Control command received via CAN
Use in this project: Used to mechanically adjust or direct the light angle based on sensor inputs.
Other applications: Robotics, camera pan-tilt systems, automatic doors, smart blinds.

## Slide 8: Information about CAN protocol:-
CAN (Controller Area Network) is a robust serial communication protocol mainly used in embedded and automotive systems. It supports multi-master communication, allowing multiple nodes to transmit data without a central controller. CAN uses differential signaling (CANH and CANL), which provides high noise immunity. It works on message-based communication, where data is identified by message IDs instead of device addresses. CAN supports data rates up to 1 Mbps in Classical CAN. It has built-in error detection and fault confinement mechanisms. Priority-based arbitration ensures that high-priority messages are transmitted first. CAN is widely used in automotive, industrial automation, and real-time control systems.

## Slide 9: Use of CAN protocol in this project:-
In this project, the CAN protocol is used to enable reliable and real-time communication between multiple lighting nodes. It allows sensor data from IR, ultrasonic, and LDR sensors to be shared across the network. CAN ensures fast and error-free data transfer even in noisy electrical environments. It helps in centralized control of multiple lights using a single controller. Priority-based messaging ensures critical control commands are transmitted first. CAN reduces wiring complexity compared to point-to-point communication. It improves system scalability by allowing easy addition of new nodes. Overall, CAN makes the smart lighting system efficient, robust, and reliable.

## Slide 10: CAN Data Frame:-

## Slide 11: Introduction to ESP32:-
ESP32 is a low-cost, low-power System-on-Chip (SoC) developed by Espressif Systems, designed for embedded and IoT applications. It features a dual-core 32-bit Tensilica Xtensa LX6 processor with integrated Wi-Fi (802.11 b/g/n) and Bluetooth (Classic + BLE). ESP32 provides rich peripherals such as GPIO, ADC, DAC, PWM, UART, SPI, I²C, I²S, and CAN (TWAI). It supports multiple power-saving modes, making it suitable for energy-efficient systems. ESP32 can be programmed using ESP-IDF or Arduino framework. Due to its high performance, connectivity, and flexibility, ESP32 is widely used in smart home, industrial, and automation projects.

## Slide 12: Why ESP32??
ESP32 is used in this project because it provides wireless connectivity (Wi-Fi/Bluetooth) for remote monitoring and control of the smart lighting system. It acts as a gateway between the CAN network and the user interface (mobile/web). ESP32 supports the CAN (TWAI) protocol, enabling direct communication with the CAN bus. Its high processing power allows data aggregation and decision making from multiple sensor nodes. Low power consumption makes it suitable for continuous operation. Overall, ESP32 adds connectivity, intelligence, and scalability to the project.

## Slide 13: Role of ESP32:-
The ESP32 acts as a gateway and communication controller in this smart lighting system. It receives sensor and control data from the CAN network. ESP32 processes this data and makes control decisions for the lighting system. It provides Wi-Fi/Bluetooth connectivity for remote monitoring and control. ESP32 sends commands back to CAN nodes to control lights and actuators. Thus, it enables smart control, connectivity, and system integration in the project.

## Slide 14: ESP32 & CAN support
ESP32 supports CAN communication through its built-in CAN controller, known as TWAI (Two-Wire Automotive Interface). It is compliant with the CAN 2.0A and CAN 2.0B standards. ESP32 does not have an internal CAN transceiver, so an external CAN transceiver (such as SN65HVD230 or MCP2551) is required. The ESP32’s GPIO pins are configured as CAN TX and CAN RX to interface with the transceiver. The TWAI driver handles message framing, arbitration, error detection, and acknowledgment. This allows ESP32 to reliably send and receive CAN messages in real-time applications.

## Slide 15: Data Flow Chart

## Slide 16: Title Lorem Ipsum
Lorem ipsum dolor sit amet, consectetuer adipiscing elit.
Nunc viverra imperdiet enim. Fusce est. Vivamus a tellus.
Pellentesque habitant morbi tristique senectus et netus.